## Slide 1: QIKcom-2 re-configurable Transponder module
Nestord Diaz-Ordaz, Bryan Hunt
Michael Segalla, & Cole Skinker
Advisor: Bob Bruninga
March 8, 2015

## Slide 2: QIKcom Team

## Slide 3: Problem Background
Automatic Packet Reporting System Protocol (APRS) is the primary communications protocol used by several USNA student satellite projects
With long development time, the response time for short fuse launch opportunities is limited
There is only one APRS satellite in operation currently

## Slide 4: Automatic Packet Reporting System (APRS)
Notes: Digital communications protocol where amateur users transmit data to passing satellites which relay that information to other users beyond the horizon
First employed in 1984 by cross-country endurance horse race for status updates and location tracking, now primarily used by amateur radio enthusiasts

## Slide 5: Host Satellite Opportunity: QIKcom-1
NovaWurks to host QIKcom1
  Provides:
    Power
    Thermal Control
    Attitude determination system
USNA provides capabilities:
  Transponder to actively notify users
  Power regulation
  Antenna release mechanism

## Slide 6: QIKcom-1 Components: Electrical Power System
Power provided by host bus. Pavg of 1.5W consistent with 1U CubeSats, however all is dedicated to telemetry rather than other subsystems
PCB Board Design
Load | Operating Voltage |  | I pk (mA) | Duty Cycle | I avg (mA) | 28V Ipk (mA) |  | 28V Iave (mA)
Beacon (Standby) | 12 |  | 15 | 98.3% | 14.75 | 7.14 |  | 7.02
Beacon (TX) | 12 |  | 600 | 1.70% | 10.2 | 260 |  | 4.86
MTT4 (TX-users) | 5 |  | 280 | 1.7% | 4.8 | 55.6 |  | 0.95
MTT4 (TX-Telemetry) | 5 |  | 280 | 4% | 11.2 | 55.6 |  | 2.2
MTT4 (RX) | 5 |  | 45 | 100% | 45 | 8.93 |  | 8.93
Power Amp (TX) | 12 |  | 600 | 10% | 60 | 260 |  | 28.6
Total |  |  |  |  |  | 647.3 |  | 52.6
28 V - Peak Power (W) |  | 18 |  |  |  |  |  | 
28 V – Average Power (W) |  | 1.5 |  |  |  |  |  | 

## Slide 7: QIKcom Components: Antenna Deployment Mechanism
Attached to EPS Board
28 V burn signal sent by host spacecraft
¼ Watt 220 Ohm resistor
Approximately 3 Watts power
Burns through fishing line constraining the antennas in about 5 seconds
20 tests conducted with 100% reliability of release

## Slide 8: QIKcom Components: Transceiver and Transponder
TX only Beacon on QIKCOM-1 notifies terrestrial users when satellite is overhead
“145.825MHzQSY 4 OPS”
Command and Control Comms card and User Transponder:
Telemetry:
QIKCOM-1>APTT4,ARISS:T#001,28V, Ibus,12V,Base_Temp,Trans_Temp,00000011

## Slide 9: QIKcom-1: Assembled Structure
Lid on Right, Baseplate on bottom
Irridite Aluminum, Emissivity: 0.11
Flathead screws with countersunk holes for smooth attachment to NovaWurks host

## Slide 10: QIKcom-1: Vibe Test
Conducted 24 Feb 2015
Shaken in X and Y axes
  Random vibe to Acceptance Levels of 10 G RMS
  Both axes lowest resonance in both directions above 400 Hz
  Satisfied the launch provider requirements
  Pre and post-test sine tests conducted at 0.5G to identify any anomalies; none detected

## Slide 11
APRS radios are expensive; Only 10% users have a radio that can use it
Yet all Amateur Radio Operators have a radio that can transmit TouchTones (DTMF)
QIKCOM-1 transition ideas to QIKCOM-2

## Slide 12
Adds DTMF (TouchTone uplink)
Text to speech + voice synthesizer
Arduino processor
Byonics MTT4B Packet Radio System
Target QIKCOM-2 for under $500
QIKCOM-2: Solution for Everyone!

## Slide 13
QIKcom2: Concept of Operations CONOPS

## Slide 14
QIKCOM-2: DTMF up and Voice down CONOPS
TX
RX
DTMF
Audio tones
Audio tones
Text-to-Speech
TT4
Voice Synthesizer
UHF TX
VHF RX
16 Character Language
APRS packet
APRS packet
Audio Waves

## Slide 15
QIKCOM-2: Those with APRS radios - CONOPS
TT4
APRS packet
DTMF Decoding
Global APRS Internet connectivity LIVE
APRS Radio
MTT4-B
Ground Stations
APRS packet

## Slide 16
Receives audio tones from amateur radios
Translates into 16 character language
$160
Parses 16-character language into APRS text packet
$30
Dual-Tone Multifrequency Decoder & TT4
DTMF
TT4

## Slide 17
Text-to-Speech chip receives APRS packet from Arduino; converts to audio-phone codes
Voice Synthesizer takes audio-phone codes and converts it to audio waves
Text-to-Voice capability for APRS users

## Slide 18
VHF Transceiver
Flexible frequency range at 145 MHz
Integrated power amp (detuned to 4W for QIKCOM-2)
Byonics.com MTT4-B Packet and Radio System

## Slide 19
These items could be added to t he QIKCOM-2 hardware to make it a standalone cubesat:
Magnetometers
Magnetotorquers
Solar Panels
Potential Cubesat Standalone Capability

## Slide 20
Questions?